## Slide 1: Antioxidant Capacity Assay for the Zivkovic’s Lab
12/1/22

## Slide 2: Antioxidant Capacity Assay
Do is yourself (Cell-free)
Dihydrorhodamine 123 (DHR)-based (Fluorescence)
  Measures HDL Anti-Oxidative capacity
  $410/several_96well_assays
  ROS indicator
  2.5 - 15 ug (cholesterol)
    HDL isolated by FPLC
  485/538 nm excitation/emission
  Pros: Cheap, published method, validated
  Cons: DHR oxidizes when exposed to air linearly between 10 and 50 min
Kit based (Cell-free)
Total Antioxidant Capacity Assay Kit (Sigma, Catalog: MAK187-1KT)
  ($532/100 tests)
  Colorimetric
  Copper based: Cu2+ ion is converted to Cu+, then Cu+ chelates with colorimetric probe
  Sample Volume: 0.01 – 1 uL serum
  90min incubation
  Pros: Quick and relatively easy
  Cons: Will this work with isolated HDL? Copper treatment will interfere with assay

## Slide 3
DHR-based assay
Stadler/Marsche, 2022
1 uL apoB-depleted serum
Kelesidis, 2011 JLR
HDL isolation: FPLC
Trakaki/Marsche, 2019
HDL isolation: Two-step density gradient

## Slide 4: PON1 Activity
Do is yourself (Cell-free)
Ca2+ dependent PON activity
  $165/several_96well_assays
  PON activity is measured by the hydrolysis of paraoxon into 4-nitrophenol
  Absorbance (405 nm)
  10 ug HDL protein
    HDL isolation by density gradient
  Pros: Cheap, published method
  Cons: Paraoxon is cheap, but toxic
Kit-based (Cell-free)
Paraoxonase 1 Activity Assay Kit (ab241044)
  $600/100tests
  Sample volume: 2-10uL serum/plasma
  Fluorescence: EX/Em = 368/460 nm
  10min incubation
  Pros: Less dangerous toxic substrate, quick and relatively easy
  Cons: Will this work with isolated HDL?

## Slide 5
Holzer/Marsche 2012
Carbamylation decreases HDL PON activity
HDL isolation: Density Gradient
HDL used: 20, ug/mL
Abcam kit